## Slide 1
Chapter Four File Systems
National University
Sacramento
CST400 Operating Systems Theory & Design
Adapted from
Andrew S. Tanenbaum. “Modern Operating Systems”. Prentice-Hall. 1992.
prepared by
Dean Hipwell

## Slide 2
Overview
Review and Preview
Files
Directories
File System Implementation
Security
Protection Mechanisms

## Slide 3
Review and Preview
Process Management
  Manages processes
  Management media: Time
Memory Management
  Manages memory
  Management media: Addresses
File Systems
  Manages files
  Management media: Names

## Slide 4
Process Management
Introduction to Processes
  An activity of some kind
  Program, Input, Output, State
Interprocess Communication (IPC)
  Busy Waiting
  Sleep & Wakeup
  Semaphores, Counters, Monitors, Messages
Classical IPC Problems
  Race conditions are Bad
  Mutual Exclusion prevents race conditions
Process Scheduling
  Share CPU time equitably, but according to priority

## Slide 5
Memory Management
Memory Management
  Organized by Addresses
  Monoprogramming versus Multiprogramming
Swapping
  Move Processes from e Memory to Disk & Back
  Fixed Partitions versus Variable
  Bit Maps, Linked Lists, Buddy System
Virtual Memory (i.e. Paging)
  Allows process size to exceed physical memory
  Pages, Frames, Page Tables, Page Faults, Associative Memory
Page Replacement Algorithms
  Optimal, NRU, FIFO, 2nd Chance, Clock, LRU, NFU, Aging
Modeling Paging Algorithms
  Belady’s Anomaly, Stack Algorithms
Design Issues for Paging Systems
  Working Set, Local/Global, Page Size
Segmentation

## Slide 6
Files
File Naming
File Structure
File Types
Files Access
File Attributes
File Operations
Memory Mapped Files

## Slide 7
File Naming
Composition
  DOS: 8 digit name, 3 digit extension
  UNIX: distinguishes between upper & lower case
  MAC: “long” file names
Extensions
  Typically mean special type of file
    More to remind the user than the computer
  Compilers may require specific extensions
    C compiler convention
      “filename.c” for input
      “filename.o” for output

## Slide 8
File Structure
Unstructured
  File is simply a sequence of bytes
  Advantage: maximum flexibility
  Disadvantage: tool complexity
  Uses: DOS and UNIX
Record Sequence
  File partitioned into fixed number of bytes
  Advantage:
    Read/Write on a single record rather than entire file
  Disadvantage: Not suited for CRT terminals
  Uses: Early card readers and CP/M
Record Tree
  Records of different length have a key field
  Records are sorted along the key field
  Advantage: Allows rapid searching
  Disadvantage: Overhead of key management
  Uses: Mainframe commercial data processing

## Slide 9
File Types
Regular Files
  Contain User information
    ASCII Text: Can be displayed and printed as is
    Binary: An Executable or Archive file
Directories
  Contain file system structure information
Character Special Files
  Model serial I/O devices
Block Special Files
  Model disks

## Slide 10
File Access
Sequential
  Start at the beginning and read to the end
  No skipping around, but rewinding okay
  Uses: Magnetic tape storage
Random
  Read bytes in any order or by using key-lookup
  Uses: Disk drive storage, databases
Starting Position
  Specified by byte count
  Seek operation looks for specific byte sequence

## Slide 11
File Attributes
Definition: Extra items about each file
Some Attributes:
  Protection
    RWX for Owner, Group, User
  Password
  Creator
  Owner
  Flags
    Read-Only, Hidden, System, Archive, ASCII/Binary, Random/Sequential, Temporary, Lock
  Record Length
  Key Position and Length
  Time
    Creation, Last Access, Last Changed
  File Size
    Current, Maximum

## Slide 12
File Operations
Create
Delete
Open
Close
Read
Write
Append
Seek
Get Attributes
Set Attributes
Rename
Copy (See page 155)
Move
Undelete
Run
Print
Associate
Call
Edit
Compress
Decompress
Load/Unload

## Slide 13
Memory Mapped Files
Maps a file into a virtual address space
Internal tables make the file a backing store
  File automatically created using page faults
Works best with segmentation
Advantage
  No Create, Open, Close, Read or Write commands
  Avoids complex and cumbersome file routines
Disadvantage
  File size automatically set to equal frame size
  Changes aren’t saved until a page is replaced
  File may be larger than page, segment, or memory size

## Slide 14
Directories
Hierarchical Directory System
Path Names
Directory Operations

## Slide 15
Root
Directories
Sub-directories
Sub-directories
Files
Hierarchical Directory System
Organizes files for easy retrieval
Typical attributes for each file
  File Name
  File Attributes
  Disk Address

## Slide 16
Path Names
Absolute
  UNIX: /usr/ast/mailbox
  DOS: c:\ccmail\user1
Working Directory
  UNIX: /usr/ast
  DOS: c:\ccmail
Relative
  UNIX: mailbox
  DOS: user1
Current Directory: “.”
Parent Directory: “..”

## Slide 17
Directory Operations
Dir
MakeDir
RemoveDir
ChangeDir
Rename
Link
Unlink
Path
Substitute
Tree
Deltree
Xcopy

## Slide 18
What disk blocks
go with what file?
File System Implementation
Implementing Files
Implementing Directories
Shared Files
Disk Space Management
File System Reliability
File System Performance

## Slide 19
Implementing Files
Contiguous Allocation
  Store files in an unbroken sequence of blocks
  Advantage
    Simple; Fast
  Disadvantage
    Max File size must be known at creation;
    Disk fragmentation is heavy
Linked List Allocation
  Store files in a linked list of blocks
    first word points to next block
  Advantage
    No fragmentation;
    Directory entries stay simple
  Disadvantage
    Random access is very slow;
    Block size is not power of 2

## Slide 20
Implementing Files
Linked List Allocation using an Index
  Store block pointers in a separate table
    File Allocation Table (FAT)
  Advantage:
    Recovers lost overhead with simple linked lists
    Random access is simplified
  Disadvantage:
    Entire table must be maintained on disk
      2 MB table for 500 MB disk
I-Nodes
  Similar to multi-level paging
    but block pointers point to tables of more pointers
  Advantage:
    Reduces space requirements for table storage
    Reduces table search time

## Slide 21
Filename
1
User
Code
3
File Type
(ext)
1
Extent
2
1
Block
Count
16 Disk Block Numbers
32 Bytes
Implementing Directories
Requirements
  ASCII filename must map to disk blocks
  File attributes must be easily retrieved
Directories in CP/M
  One and only one directory
  Disk block numbers stored with directory entry
  Each entry points to up to 16 blocks

## Slide 22
Filename
3
File Type
(ext)
1
Attributes
10
Reserved
2
2
2
4
Time
Date
1st
Block
Number
Size
32 Bytes
To
File
Allocation
Table
Implementing Directories
Directories in MS-DOS
  Directory entries are 32 bytes long
  First block number indexes into the FAT
  Subsequent blocks are recovered from the FAT

## Slide 23
Filename (14)
I-Node
Number
2
16 Bytes
.
1
..
1
bin
4
lib
14
usr
6
Root Dir
Table
mode
size
times
132
...
/usr
I-Node 6
.
6
..
1
dick
19
erik
30
ast
26
/usr Dir
Block 132
mode
size
times
406
...
/usr/ast
I-Node 26
.
26
..
6
grant
64
book
92
mbox
60
/usr/ast Dir
Block 406
Example: Look up “/usr/ast/mbox”
Implementing Directories
Directories in UNIX
  Directory entries are 16 bytes long
  I-Node number indexes to other I-Nodes
  I-Nodes index to sub-directories

## Slide 24
One file in
two directories
Shared Files
Approach
  Allows single file to appear in multiple directories
  Connections are called links
  Trees become “Directed Acyclic Graphs”

## Slide 25
Shared Files
Problem
  Appended blocks may only appear in the owner’s directory structure
Solution 1:
  Create a small data structure associated with each file
  Stores block numbers in the structure, not the directory
  May result in accesses to invalid I-nodes
Solution 2: Symbolic Linking
  Use the same path and filename, but of file type “Link”
  When a non-owner accesses the filename, the O/S reads via the link to the original file
  Requires overhead to store and follow path to original file

## Slide 26
Disk Space Management
General Strategies
  Consecutive Bytes
    Growth forces Move
  Blocks
    Growth does not force Move
Block Size
Keeping Track of Free Blocks
Disk Quotas

## Slide 27
Sectors
Tracks
Cylinders
Page Size
Key Parameters

## Slide 28
200
150
100
50
100
75
50
25
128
256
512
1K
2K
4K
8K
Block Size (bytes)
Data Rate (KB/sec)
Disk Utilization (percent)
Assuming all files consist of 1K pages:
Block Size

## Slide 29
Keeping Track of Free Blocks
Linked List
  Start with a “Free” list
  Each entry points to a “free” block on disk
  With a 16-bit list entry, a 1K block holds 512 entries
  With 1024 blocks per MB, need 2 blocks per MB
Bit Map
  For n blocks, build a map containing n bits
  Each bit is set when corresponding block is free
  Assuming 1K block size, need 1024 bits per MB
Difference
  “Free” list shrinks as blocks are used
    bit maps don’t

## Slide 30
filename
attributes
disk address
uid=8
Quota Pointer
filename
attributes
disk address
uid=9
Quota Pointer
“Open File” table
Soft Block Limit
Hard Block Limit
Current # of Blocks
Block Warnings Left
Soft File Limit
Hard File Limit
Current # of Files
File Warnings Left
“Quota” table
Disk Quotas
Approach
  System Administrator assigns maximum space per user
  Operating System enforces the quotas

## Slide 31
File System Reliability
Concepts
  Losing a file also losses information
  File system helps protect information
Bad Block Management
Backups
File System Consistency

## Slide 32
Bad Block Management
Problem
  Disk manufacturers cannot guarantee 100% defect free on 100% of all disks
  Disks become unreliable with use
Hardware Solution:
  “Bad” Block List maintained on each disk
Software Solution:
  “Bad” Block File created to isolate blocks
  Removes bad blocks from “Free” list
  Watch out during disk backups

## Slide 33
Backups
Disk Dumps
  Disk Copy
    Okay for floppies
  Tape Backups
    Slow and include “Bad” block files
  Removable Hard Drive
    Syquest, Zip, Jazz
Incremental Dumps
  Data Files Only
  Modified Files Only
  Full Dumps periodically
Archive Bit
  Set when a file is modified
  Reset when a file is backed up

## Slide 34
File System Consistency
Problem
  System crashes in the middle of a write operation leave files in an unstable state
Solution:
  Block Consistency Check
    Counter 1: Block is allocated to Files
    Counter 2: Block is listed as “Free”
  File Consistency Check
    Counter 1: I-Node is pointed to by Directories
    Counter 2: Link counts stored in the I-Nodes

## Slide 35
1
1
0
1
0
1
0
0
0
0
1
0
1
1
2
1
1
0
0
1
0
0
1
0
0
0
1
1
1
2
0
1
0
0
0
0
0
1
1
1
In Use
Free
Blocks
Okay
Missing
Block
Duplicate
Free Block
Duplicate
Data Block
Duplicate
Listing
Block Consistency Check

## Slide 36
8
7
11
3
5
8
6
10
2
4
3
1
8
5
9
13
9
2
8
7
11
3
5
8
6
10
4
4
3
1
8
5
9
13
9
1
Directory
Files
Link Counts
I-Nodes
Okay
Too Many
Links
Too Few
Links
10
10
8
8
File Consistency Check

## Slide 37
File System Performance
Problem
  RAM access takes ~100 nanosec
  Disk access takes ~100 millisec
Improvement #1: Cache
  RAM is used to buffer disk accesses
  Buffers store blocks of information
  Block replacement uses same algorithms as Paging
  Cache references less frequent than with Paging
Drawbacks
  Disk crashes impact more than one file or directory
  Some blocks are rarely referenced

## Slide 38
Block Replacement
Adjustment
  Is the block likely to be needed again soon?
  Is the block essential for consistency?
Approach
  Unneeded blocks go to the head of the list
    They are reused first
  Blocks needed soon go to the tail of the list
    They are reused last
  Blocks affecting consistency get written to disk
  All blocks get written to disk periodically
    UNIX: “Sync” system call every 30 seconds
    DOS: Write modified blocks immediately
      Write-Through Cache

## Slide 39
File System Performance
Improvement #2: Reduce Disk Arm Motion
  Write sequential blocks to same cylinder
  Bit Map block management faster than Linked List
  Improve Linked Lists by allocating Clusters
Improvement #3: Rotational Positioning
  Interleave sequential blocks depending on:
    Disk rotational period 16 msec
    User request turnaround time: 4 msec
    e.g. Next block is one cylinder away, but a quarter the way around
Improvement #4: I-Node Placement
  Normal: I-Nodes at start of disk
  Better: I-Nodes in the middle of the disk
  Advantage: Reduces average seek time to next cylinder

## Slide 40
Security
The Security Environment
Famous Security Flaws
The Internet Worm
Generic Security Attacks
  Common Approaches
  Viruses
Design Principles for Security
User Authentication
  Passwords
  Physical Identification
  Countermeasures
  Monitoring

## Slide 41
The Security Environment
Security
  Prevent modification by unauthorized Persons
Protection
  Prevent modification by unauthorized Processes
Protection Mechanisms
  O/S mechanisms to safeguard information
Facets
  Data Loss
    Acts of God
    System Malfunctions
    Human Error
  Intruders
    Passive
    Active or Malicious
  Privacy: protecting individual rights

## Slide 42
Famous Security Flaws
lpr -r printed a file, then removed it
Attack the password file
  Overwrite the password file using a core dump
  Intercept mkdir just before the chown command
Bypass security protocols
  batch file into the victim directory
  Modify a tool -- Trojan Horse
  Use security feedback to help identify password letters
  Interfere with password checking algorithms
    After confirmation, but before retrieval, overwrite a verified filename with the victim’s filename

## Slide 43
The Internet Worm
Self-Replicating Program
  Bootstrap program: “l1.c”
  Worm program
Approach
  Send the bootstrap ahead and run it
  Have the bootstrap go back and get the Worm
  The Worm would try to break user passwords
  Stop the Worm if one was already present
Infection Methods
  Run a remote shell
  Exploit the finger daemon
  Use sendmail to pass the bootstrap routine

## Slide 44
Generic Security Attacks
Common Approaches
  Read core dumps
  Illegal system calls or parameters
  Interrupt the login sequence
  Modify complex O/S structures
  Spoof the user by using a phony login program
  Execute somebody else’s prototype code
  Build in a trapdoor
  Trick the director’s secretary
Cures
  Good security practices

## Slide 45
Generic Security Attacks
Viruses
  Program fragment attached to legitimate program
  Fragment runs first when legitimate program executes
  Finds uninfected program and attaches itself
  Symptoms
    Erase, corrupt, or encrypt files
    Fill-up disk space or RAM
    Change the display
    Prevent normal operation
Cures
  Clean infected files
  Reformat the disk
  Use checksums
  Write protect binary files

## Slide 46
Design Principles for Security
Make the design available to the public
Default state should prevent access
Check for current permission
  not simply once at the beginning
Least privilege possible
Protection mechanisms should be built-in
  not add-ons
Keep it simple for legitimate users

## Slide 47
User Authentication
Passwords
  Easy to implement
  Easy to defeat
Variations on Passwords
  Randomly selected characters
  Salting the password file
  Computer generated advice (e.g. “fotally”)
  Change frequently
  One-Time passwords
  User generated test questions
  Challenge-Response algorithms

## Slide 48
User Authentication
Physical Identification
  Fingerprints, Finger Lengths
  Voiceprint
  Signature Analysis
  Retinal Scans
Countermeasures
  Restrict the user to a terminal, time, or day
  Immediate call-back
  Record all login attempts
  Baited Traps
Monitoring
  Frequent disk searches
  User profiling

## Slide 49
Protection Mechanisms
Protection Domains
  Definition
    A set of (object, rights) pairs
  Each process runs in a protection domain
  Processes can switch domains
    but not be in two domains at once
  Shared peripherals can be written to
    but not read
  Application: Multiple security levels
    Government, Banking, Insurance
  Disadvantage:
    File duplication
    Protection matrices are sparse
    Schemes must also be implemented by tools

## Slide 50
(Jan,*)
(Jan,sys)
(Els,stf)
(Maike,*)
(*,stu)
(Jelle,*)
File0
File1
File2
File3
File4
Prt1
Prt2
Dom1
Dom3
Dom2
r
rw
e
r
rwx
rw
w
e
rw
rwx
w
w
rw
r
rw
r
w
Domains
Objects
Protection Domain

## Slide 51
  Column by Column
  Shows which domains have “access” to each object
File0
File1
File2
File3
File4
Prt1
Prt2
Dom1
Dom2
(Jan,*), r
(Jan,*), rw
(Jan,*), e
(Jan,sys), r
(Jan,sys), rwx
(Jan,sys), rw
(Jan,sys), w
(Jan,sys), e
(Els,stf), rw
(Els,stf), rwx
(Els,stf), w
(Els,stf), w
(Maike,*), rw
(*,stu), r
(Jelle,*), rw
(Jelle,*), r
(Jelle,*), w
Dom3
Access Control List

## Slide 52
  Row by Row
  Shows which objects can be “accessed” by a domain
(Jan,*)
(Jan,sys)
(Els,stf)
(Maike,*)
(*,stu)
(Jelle,*)
File0, r
File1, rw
Dom2, e
File2, r
File3, rwx
File4, rw
Prt1, w
Dom1, e
File2, rw
File4, rwx
Prt1, w
Prt2, w
File0, rw
File2, r
File0, rw
File2, r
Prt2, w
Capabilities Control List

## Slide 53
Protection Mechanisms
Protection Models
  Primitives can be combined into commands
    Create or Delete a domain, an object, or a right
  Commands must not allow an unauthorized state
  Difficult to Prove
Covert Channels
  Definition
    Recovering information by indirect means
  Monitoring CPU usage
  Monitoring the page fault rate
  Monitoring peripheral access

## Slide 54
Summary
Files, Directories, and Disks
  Files
    Naming, Structures, Types, Attributes, Operations
  Directories
    Hierarchical, Path Names, Operations
File System Implementation
  Contiguous, Linked List, I-Node
  Disk Space Management
    Block Size, Free Blocks, Bad Blocks, Disk Quotas
  Consistency Checking
  Performance
    Cache, Disk Control & Format choices
Security
  Data Loss, Intruders, Privacy, Viruses, Worms
Protection Mechanisms
  Domain Control Tables